## Slide 1: Continuity in Arc Connections
For the Geometry Library
2024-06-29 by S. Brennan

## Slide 2: There are 3 types of continuity commonly used on roads
C0 –arcs connect at ends
C1 – arcs are tangent to each other, connected by line segments e.g. slope continuity
C2 – arcs connect by spirals, e.g. curvature continuity

## Slide 3: This presentation will show that the requirements for continuity are related to the radii, r1 and r2, and signed distance between the centers of circles 1 and 2, d12
These conditions have geometric meaning in plots of r2 versus d12

## Slide 4: We define the signed distance from 1 to 2, d12, as the center-center distance between a starting circle (green) and ending circle (red).
Start, 1
End, 2
Positive d12
Start, 1
End, 2
Negative d12
Note that circles both are counter-clockwise in the arc direction (CCW). The sign (+ or -) of d1s, discussed in the next slides, depends on the direction of the arcs around the circle and the points of departure from circle 1 to circle 2.

## Slide 5: The sign is necessary because there are often 2 possible continuity solutions, but only one will be valid
Examine the vectors from the center of circle1 to the valid departure point on 1, Vc1d1, and the vector from the center of circle1 to the center of circle2, Vc1c2. The cross product, Vc1d1 x Vc1c2, will be positive in the z-component if d12 is positive.
Start, 1
End, 2
Positive d12
Start, 1
End, 2
Negative d12
Candidate departure
point on circle 1
Candidate departure
point on circle 1

## Slide 6: So, to determine the sign of the distance between centers, we need to know the candidate departure point on arc1. The best estimate for this is usually the end of arc1.
Start, 1
End, 2
Positive d12
Start, 1
End, 2
Negative d12
Candidate departure
point on circle 1
Candidate departure
point on circle 1

## Slide 7: C0 continuity conditions

## Slide 8: For C0 continuity, the arcs must intersect. In order for the arcs to intersect, the circles must intersect.
Note: C0 continuity does not depend on the rotation direction of the circles. The circles simply must intersect
Start, 1
End, 2
Start, 1
End, 2

## Slide 9: To intersect, the circles must be close to each other
Close means that d12 must be less than r1+r2, or d12<r1 + r2
Start, 1
End, 2
d12

## Slide 10: As well, circle 1 cannot be inside circle 2 or circle 2 inside circle 1
So d12>r2 – r1, and d12>r1-r2
End, 2
Start, 1
d12
Start, 1
End, 2
d12

## Slide 11: If we plot these conditions using in r2 on the x-axis, and d12 on the y-axis, they form lines defining a region
d12
r2
d12=r1 + r2
r1
r1
d12=r2 – r1
d12=r1-r2
Region of C0 continuity

## Slide 12: Notice that, if we have a situation where arc2 is not feasibly C0 connected to arc1, the diagram indicates which direction to modify, and by how much, to create feasibility
d12
r2
r1
r1
Region of C0 continuity
Direction and distance to move in r2 and d12 directions to force C0 continuity by modifying arc2

## Slide 13: C1 continuity conditions

## Slide 14: For C1 continuity, the arcs must allow a tangent line between them. If the arcs intersect, the traversal direction around the arc (CW or CCW) must be the same.
So C1 continuity does depend on the rotation direction of the circles.
Start, 1
End, 2
Tangent possible
If both CCW or CW
Start, 1
End, 2
Tangent possible
Start, 1
End, 2
Tangent possible
If one CCW and other CW
Start, 1
End, 2
Tangent NOT possible
d12>r2 + r1

## Slide 15: As well, for any tangents, circle 1 cannot be inside circle 2 or circle 2 inside circle 1
So d12>r2 – r1, and d12>r1-r2
End, 2
Start, 1
d12
Start, 1
End, 2
d12

## Slide 16: If we plot these conditions using in r2 on the x-axis, and d12 on the y-axis, they form lines defining a region
d12
r2
d12=r1 + r2
r1
r1
d12=r2 – r1
d12=r1-r2
Region of C1 continuity, both CCW or CW
Region of C1 continuity, if one CCW and other CW

## Slide 17: C2 continuity conditions

## Slide 18: For C2 continuity, the arcs must connect by spirals. This is only possible if one arc is inside the other if the traversal direction around the arc (CW or CCW) is the same.
So C2 continuity does depend on the rotation direction of the circles.
Spiral possible
If both CCW or CW
Start, 1
End, 2
Spiral NOT possible
Start, 1
End, 2
Spiral possible
If one CCW and other CW
Start, 1
End, 2
Spiral NOT possible

## Slide 19: If we plot these conditions using in r2 on the x-axis, and d12 on the y-axis, they form lines defining a region
d12
r2
d12=r1 + r2
r1
r1
d12=r2 – r1
d12=r1-r2
Region of C2 continuity, both CCW or CW
Region of C2 continuity, if one CCW and other CW

## Slide 20: Note, of both arcs are oriented same direction, then C2 continuity covers exactly the OPPOSITE region as that for C1 continuity. Thus, for these arcs, it is impossible to design joints between arcs such that they can be both C1 and C2 continuous at same time.

## Slide 21: Other useful metrics

## Slide 22: There are often situations where 2 arcs are nearly the same, and it may be useful to measure the minimum change to merge them as 1 arc.
The distance of the query point to the [r1 0] position defines the minimum arc2 needs to change, or twice the distance that both arc1 and arc2 would change equally.
d12
r2
d12=r1 + r2
r1
r1
d12=r1-r2
Two arcs are almost identical (common situation)
Minimum change